## Slide 1
Q2 STATUS UPDATE
IoT Programmable Blocks
A Modular, Semantically-Composable IoT Automation Platform with Agentic AI Code Generation
Project Team: G-30-CSE-19B
Department: Computer Science & Engineering
Date: July 2026
Notes: Welcome everyone to our Q2 status update for the IoT Programmable Blocks project. We're here to share our progress on revolutionizing how users interact with IoT systems, moving beyond complex, low-level programming. Our core message today is about creating a modular, AI-augmented platform that makes real-world automation accessible to everyone. We'll dive into the technical advancements and the integration of agentic AI that makes this possible.

## Slide 2
Agenda
01
Introduction & Problem Statement
02
System Architecture Overview
03
Hardware & Firmware Milestones
04
Communication & Control Layer
05
AI Integration: DeepSeek Agentic Chatbot
06
Experimental Results & Evaluation
07
Future Roadmap & Conclusion
Notes: So, what's on the agenda for today? We'll start by framing the problem we're solving, then move through the technical stack from our custom hardware to the AI integration. This includes a deep dive into our system architecture, the milestones we've hit in hardware and firmware, and how our AI chatbot is bringing natural language to automation. We'll wrap up with our experimental results and a look at what's next. This journey will show you how we're making IoT programming intuitive and powerful.

## Slide 3
Problem Statement
The IoT Programming Inaccessibility
Vendor Lock-in: Devices are often tied to proprietary ecosystems (HomeKit, Alexa, SmartThings), limiting cross-platform flexibility.
High Complexity: Fragmented models demand unique SDKs and management of low-level details like WiFi provisioning.
Semantic Gap: Simple logical intents require hundreds of lines of code across firmware, servers, and clients.
RESEARCH QUESTION
"Can we design a modular IoT platform where physical blocks are
abstracted as first-class software objects, and automation scripts are
autonomously synthesized from natural language by an agentic LLM?"
Notes: Building on our agenda, let's start with the fundamental problem we're tackling: the inaccessibility of IoT programming. Today's IoT landscape is plagued by vendor lock-in, forcing users into proprietary ecosystems, and overwhelming complexity, demanding unique SDKs for every device. This creates a huge semantic gap where even simple logic requires excessive code. Our research question asks if we can abstract physical blocks as software objects and synthesize scripts from natural language, truly bridging this gap. We believe this approach will unlock a new era of intuitive automation.

## Slide 4
System Architecture
A Three-Tier Modular Design
TIER
TECHNOLOGY
RESPONSIBILITY
Presentation
React, React Flow, DeepSeek API
User interface, flow visualization, chatbot interaction
Control
Python 3.13, blocks.py
Device orchestration, script execution, AI tool-calling
Physical
ESP8266, C++/Arduino
Sensor reading, actuator control, local REST API
Connectivity Milestones
Dual-Mode WiFi: Simultaneous AP + Station Mode (WIFI_AP_STA) for easy provisioning.
Zero-Config: mDNS-based discovery for automatic host resolution without manual IP entry.
Notes: To address that problem, we've designed a robust, three-tier modular architecture. This structure separates concerns, making the system scalable and maintainable. The physical tier comprises our custom ESP8266-based hardware blocks, each with its own local RESTful API. Above that, the control tier, powered by Python, orchestrates device management and executes logic. Finally, the presentation tier, a React-based web portal, provides the user interface and integrates our AI chatbot. This tiered approach, combined with dual-mode WiFi and mDNS discovery, ensures seamless connectivity and a smooth user experience. Now, let's look closer at the physical tier and how we've abstracted our hardware.

## Slide 5
Hardware Design
Modular Block Abstraction
Block Type
Physical Component
Direction
LED
5mm LED + 220Ω Resistor
Output
Buzzer
Piezoelectric Buzzer
Output
Button
Tactile Push-button
Input
Temperature
DS18B20 (OneWire)
Sensor
Relay
5V Relay Module
Power Output
Key Design Principle: Uniformity
Uniform API Surface: Every block exposes identical REST endpoints regardless of physical function.
Hardware Agnostic: Abstraction hides GPIO complexity, allowing the control layer to treat all blocks polymorphically.
Self-Contained: Each block is an independent ESP8266 module with its own local intelligence.
Notes: Moving from our overall architecture, a core innovation lies in our modular block abstraction at the hardware level. We've established a uniform interface for heterogeneous hardware, meaning every block, whether it's an LED, a button, or a temperature sensor, exposes an identical API surface. This is a game-changer because it allows our software layers to interact with any hardware block polymorphically, greatly simplifying integration. We're abstracting away the complexity of physical GPIO pins behind high-level REST endpoints, making each block a self-contained, intelligent module. This uniformity is key to our platform's flexibility and ease of use.

## Slide 6
Firmware & Connectivity
Robust Networking Features
Dual-Mode WiFi: Simultaneous AP + Station mode for local config and cloud sync.
Captive Portal: Zero-code WiFi provisioning via 192.168.4.1.
mDNS Discovery: Zero-config resolution (e.g., iot-block-002.local).
Persistence: EEPROM storage for WiFi credentials and device state.
Remote Sync Protocol
Bidirectional State Synchronization
PULL (Every 500ms): Device fetches desired state from cloud API and updates local outputs.
PUSH (On Change): Device reports sensor data and local state changes to the server (min 200ms).
Notes: Our firmware is all about robust networking and local intelligence. We've engineered it for reliability and ease of use. The dual-mode WiFi lets devices connect to the internet while also acting as a local access point. This means you can easily configure them from your phone or laptop. We also have a clever sync protocol that keeps the cloud and local states perfectly aligned. This ensures minimal latency and a smooth user experience. Next, we'll see how this robust firmware enables our Python control layer.

## Slide 7
Python Control Layer
OOP Orchestration & Abstraction
First-Class Objects: Physical blocks are elevated to Python objects, hiding HTTP complexity.
Deduplication: State-aware logic avoids redundant network calls to the hardware.
Parallel Discovery: Scans 255 mDNS hosts in <3s using multi-threaded execution.
DECLARATIVE AUTOMATION LOGIC
from blocks import LED, Button button = Button("IoT-Block-001") led = LED("IoT-Block-002") if button.state: led.on() # HTTP POST /api/io/set else: led.off()
Notes: The Python control layer is where the magic happens. We've elevated physical blocks into first-class Python objects. This makes automation scripts incredibly readable and intuitive. Our system also intelligently deduplicates network calls, avoiding redundant communication with the hardware. We've optimized device discovery too, scanning 255 hosts in under three seconds. This ensures a responsive experience, even with many devices on the network. Now, let's explore how AI integrates with this powerful control layer.

## Slide 8
DeepSeek Agentic Chatbot
Engine: DeepSeek-V3 (128K Context)
Translating Intent into Action
Autonomous Synthesis: Translates natural language prompts into executable Python automation scripts.
Bidirectional Sync: Automatically updates visual flow diagrams based on generated script logic.
Tool-Calling: Directly interacts with physical hardware I/O for real-time state discovery and control.
SAFETY & EXECUTION CONSTRAINTS
Sandboxed execution environment for all AI-generated scripts.
Schema-validated tool outputs to prevent hardware command injection.
Mandatory error handling and KeyboardInterrupt termination in all scripts.
Notes: Our AI integration is a true game-changer. We're using DeepSeek-V3 to translate natural language into executable Python scripts. This means users can simply describe what they want to happen, and the AI generates the code. It's not just about code generation; the AI also synchronizes with our visual flow diagrams. Plus, it can directly interact with the hardware in real-time. We've also built in robust safety measures, including sandboxed execution and schema-validated outputs. This ensures secure and reliable operation. This powerful AI then feeds into our user-friendly web portal.

## Slide 9
Web Portal & Visual Programming
Stack: React 18 + React Flow + Tailwind
Unified Runtime Administration
Real-Time Monitoring: Live state management and health tracking of all discovered hardware blocks.
Bidirectional Sync: Changes in the visual graph update the Python script, and vice versa.
Integrated Chatbot: Direct access to the DeepSeek agent for rapid prototyping and script synthesis.
VISUAL FLOW BUILDER
Node-edge graph representation of block interactions and automation logic.
Dynamic recomposition of automation flows without manual code editing.
Responsive design optimized for both desktop and mobile administration.
Notes: The web portal is your command center for the entire system. It provides real-time monitoring of all your discovered hardware blocks. You get a live view of their status and health. The portal features a visual flow builder, allowing you to see and manipulate your automation logic. Changes you make in the visual graph instantly update the underlying Python script, and vice versa. And with the integrated chatbot, you can rapidly prototype new automations using our DeepSeek agent. This responsive design works great on both desktop and mobile. Now, let's look at the performance benchmarks for all these components.

## Slide 10
Experimental Results
Performance Benchmarks
METRIC
MEASURED VALUE
Discovery Time (255 Hosts)
< 3.0 Seconds
Local HTTP API Latency
< 15 Milliseconds
Remote Sync Latency
80 - 200 Milliseconds
AI Script Synthesis Time
< 3.0 Seconds
Success Scenarios
✓ Button → LED Relay: Physical trigger to remote actuation in < 50ms.
✓ Agentic Logic: 95% accuracy in translating natural language to valid Python scripts.
✓ Flow Sync: 100% consistency between generated code and visual graph updates.
Notes: Now, let's look at what we've achieved. Our experimental results confirm the platform's efficiency and the AI's accuracy. We've seen very fast response times for local interactions. Our AI agent correctly generates complex scripts almost every time. And the visual flow diagram always stays perfectly in sync with the code. This means we're delivering a highly responsive and reliable system. These strong results set us up well for our next steps.

## Slide 11
Challenges & Roadmap
CURRENT LIMITATIONS
Hardware Constraints: v1 blocks are single-role per ESP8266; limited RAM for complex local logic.
Sync Overhead: HTTP polling introduces latency and network noise compared to push-based models.
Security: Lack of encrypted local communication (roadmap item for v2).
Q3: INFRASTRUCTURE
ESP32 Migration: TLS/HTTPS support and BLE mesh networking.
WebSocket Push: Sub-10ms state sync latency.
Q4: INTELLIGENCE
Multi-Agent: Collaborative distributed automation.
Formal Verification: Safety checking for AI scripts.
Notes: While our results are strong, we also have a clear understanding of our current limitations and a solid plan to address them. Our initial hardware has some constraints, and our current synchronization method can introduce latency. We're moving to ESP32 boards for more power and better security. We'll also switch to WebSockets for near-instant state updates. And we're exploring advanced AI features like multi-agent collaboration and formal verification to ensure safety. This roadmap will push the boundaries of what our platform can do.

## Slide 12
PROJECT WRAP-UP
Final Remarks
Summary of Achievements
Modular Platform: Successfully designed a hardware-agnostic IoT system with uniform REST APIs.
OOP Control: Developed a robust Python library for declarative, state-aware device orchestration.
AI Integration: Integrated agentic AI for natural language automation script synthesis.
Visual Programming: Built a bidirectional flow environment synchronized with code logic.
Thank You!
QUESTIONS & DISCUSSION
Notes: In summary, we've made significant progress this quarter. We've built a truly modular and hardware-agnostic IoT platform. Our Python control layer makes automation intuitive and powerful. And our agentic AI integration allows users to create complex automations with natural language. We've also created a visual programming environment that keeps everything in sync. Thank you for your time and attention. I'm happy to answer any questions you might have.